## Slide 1: Activity 2
MQTT Protocol
Hélio Nakazato
Hirley Dayan

## Slide 2: MQTT QoS 2 Message Flow (A method)
Publisher
Server
Subscriber
PUB QoS2 PID1
PUBREC PID1
PUBREL PID1
PUB PID1
PUBCOMP PID1
Other publishes related to other PIDs may happen during this interval before PUBREL

## Slide 3: MQTT QoS 2 Message Flow (B method)
Publisher
Server
Subscriber
PUB QoS2 PID1
PUBREC PID1
PUBREL PID1
PUB PID1
PUBCOMP PID1
Other publishes related to other PIDs may happen during this interval before PUBREL
PUB PID1 Message Discarded

## Slide 4: Differences Between QoS1 vs QoS2 on MQTT
In QoS1 messages are sent at least once to the receiver. Once PUBLISH is sent with packet ID, the sender waits for an acknowledge with PUBACK message, with same packed ID of the published message. Until the reception of PUBACK message, the sent PUBLISH information is kept on ”unacknowledged” status.
In QoS2, the PUBLISH message is kept on ”unacknowledged” status until the PUBREC message is received from the server with same packet ID of the published message. Having received a PUCREC from the server, the sender sends a PUBREL messages, releasing the message to the subscribers, and it is kept on "unacknowledged" status until message PUBCOMP is received from the server. The use of PUBREL and PUBCOMP messages depends on which method is chosen to be used. There are two methods of choice for using PUBREL and PUBCOMP messages. On method A, the server receives a PUBLISH message and does not releases it until PUBREL is received. On method B the server releases the PUBLISH message once it receives and discards it once a PUBREL is received
QoS2 is used when duplicated or lost messages is not acceptable, assuring the delivery of the message, but on the other hand does not deliver a good performance as when using QoS0 or QoS1.

## Slide 5: MQTT vs MQTT-SN
MQTT/SN is a lightweight protocol based on MQTT for Wireless Sensor Networks (WSN) with:
  low bandwidth
  link failures
  short message requirements
  among others

## Slide 6: MQTT vs MQTT-SN
 |  | MQTT | MQTT-SN
Message length |  |  | 
 | CONNECT | Simple message with will topics and and will message if applicable | 3 messages, will topics and will message are optional and can be send on other 2 CONNECT MESSAGE
 | PUBLISH | Topic name of any length, no topic ID concept | Short two-bytes long topic ID as ”topic name”
 |  |  | Registration procedure to register chosen short topic name for topic ID
 |  |  | No registration is required for topic IDs and short topic names already introduced

## Slide 7: MQTT vs MQTT-SN
 |  | MQTT | MQTT-SN
Message length |  |  | 
 | PUBLIC | Topic name of any length | Short topic name definition, with a length limit of two octets.
Will Topic and Message |  | Discarded during DISCONNECT | Can be modified during a session
Sleeping clients support |  | Clean session(?) | Message buffering during the time clients are sleeping
Transport Type |  | Reliable point-to-point | Unreliable datagrams
Communication |  | TCP/IP | Non-IP or UDP
Min/Max Message Sizes |  | 2 Bytes / =< 24 MBytes | 1 Byte / 128 Bytes